## Slide 1: OFDM Project
Submitted to: Dr. Mohamed Khairy Eng. Mohamed Khaled
Presented by : Team 46

## Slide 2: Team Members & Roles
Name | ID | SEC | ROLE
احمد ابراهيم حسن ابراهيم | 9220014 | 1 | (Q3) OFDM
احمد خلف محمد على | 9220036 | 1 | (Q1) & (Q2) BPSK
احمد محمد إبراهيم | 9220078 | 1 | (Q2) QPSK & 16-QAM
Team : 46

## Slide 3: Execution time of DFT and FFT

## Slide 4: Execution time comparison
Execution time comparison
The FFT provides significantly superior performance compared to the direct DFT implementation in terms of execution time.
The FFT is the preferred method for computing the Fourier transform of large signals

## Slide 5: Code
function X_k = DFT_function(X_n) N=length(X_n); X_k=zeros(1,N); for k = 1:N-1 for n = 1:N-1 X_k(k+1) = X_k(k+1) + X_n(n+1) * exp((-1i*2*pi*n)/N); end end end
DFT Implementation:
Test Signal Generation:
L= 4096; X_N = rand(1,L);

## Slide 6: Code
% count time taken for DFT tic; X_K_DFT= DFT_function(X_N); taken_time_DFT=toc; % count timw taken for fft tic; X_K_fft= fft(X_N); taken_time_fft=toc;
Execution Time Measurement:
Result:
% print time taken for DFT and fft fprintf("DFT excution time : %.6f seconds\n",taken_time_DFT); fprintf("fft excution time : %.6f seconds\n",taken_time_fft); % Bar Graph times = [taken_time_DFT, taken_time_fft]; x=["DFT" "FFT"]; figure; b = bar(x, times); % <-- store bar handle grid on; ylabel('Execution Time (seconds)'); xlabel('type of transformer'); title('Execution Time Comparison: DFT vs FFT');

## Slide 7: BER performance for BPSK and 16-QAM over Rayleigh flat fading channel

## Slide 8: BPSK BER Over Rayleigh Channel
BPSK BER Over Rayleigh Channel
The BER for repetition-5 is significantly better than that of normal bpsk.
In this case, an error occurs only if three or more bits are changed, which is much less likely than a single-bit error in normal bpsk.

## Slide 9: QPSK BER over Rayleigh Channel
QPSK BER Over Rayleigh Channel
The next curve shows the performance comparison between normal QPSK and repetition-5 QPSK. As expected, QPSK with repetition-5 demonstrates better performance.
Comparing BPSK and QPSK BER over rayleigh channel, we can see that the difference in BER between the two cases is relatively small.

## Slide 10: 16-QAM BER over Rayleigh Channel
As the modulation order increases, the BER also increases. This occurs because higher-order constellations have more symbols, which reduces the distance between points and tightens the decision boundaries, making the system more sensitive to noise.
On the other hand, higher-order modulation provides a higher data rate. For example, 16-QAM transmits at four times the rate of BPSK and twice the rate of QPSK.
16-QAM BER Over Rayleigh Channel

## Slide 11: BPSK,QPSK and 16-QAM BER Over Rayleigh Channel
BPSK,QPSK and 16-QAM BER Over Rayleigh Channel
The BER performance of BPSK and QPSK is almost identical; however, QPSK is preferred due to its higher data rate. On the other hand, 16-QAM exhibits the worst BER performance, but it provides a higher data rate than both BPSK and QPSK.
The BPSK and QPSK repetition 5 curves are not the same.

## Slide 12: Code
Bitstream Generation:
% Set number of bits based on modulation switch upper(modulation_type) case 'BPSK' Num_bits = 5e6; bits_per_symbol = 1; case 'QPSK' Num_bits = 5e5; bits_per_symbol = 2; case '16QAM' Num_bits = 1.2e6; bits_per_symbol = 4; otherwise error('Unsupported modulation type'); end fprintf('Running %s simulation with repetition factor = %d...\n', modulation_type, repetition_factor); % Generate original bits (column vector) Tx_bits = randi([0 1], Num_bits, 1);

## Slide 13: Code - Transmitter
function bits_rep = encode_bits(bits, repetition_factor) % Repeat each bit 'repetition_factor' times bits_rep = repelem(bits, repetition_factor); end
Repetition Encodin:
Modulation:
function symbols = map_bits(bits, modulation) % Maps bits to symbols based on modulation switch upper(modulation) case 'BPSK' symbols = 2*bits - 1; % 0->-1, 1->1 case 'QPSK' b1 = bits(1:2:end-1); b2 = bits(2:2:end); symbols = complex(2*b1-1, 2*b2-1); case '16QAM' % 16-QAM Gray Mapping bits = bits(:); b = reshape(bits,4,[]).’; gray = zeros(size(b)); gray(:,1) = b(:,1); gray(:,2) = xor(b(:,1),b(:,2)); gray(:,3) = xor(b(:,2),b(:,3));

## Slide 14: Code - Transmitter
gray(:,4) = xor(b(:,3),b(:,4)); idx = bi2de(gray,'left-msb')+1; % 16-QAM constellation (normalized) I_levels = [-3 -1 3 1]; Q_levels = [-3 -1 3 1]; const = zeros(16,1); for k=0:15 bin_k = de2bi(k,4,'left-msb'); bin_nat = zeros(size(bin_k)); bin_nat(1) = bin_k(1); bin_nat(2) = xor(bin_nat(1), bin_k(2)); bin_nat(3) = xor(bin_nat(2), bin_k(3)); bin_nat(4) = xor(bin_nat(3), bin_k(4)); i_idx = bi2de(bin_nat(1:2),'left-msb')+1; q_idx = bi2de(bin_nat(3:4),'left-msb')+1; const(k+1) = I_levels(i_idx)+1j*Q_levels(q_idx); end const = const/sqrt(mean(abs(const).^2)); symbols = const(idx).'; otherwise error('Unsupported modulation type'); end end
Modulation:

## Slide 15: Code - Transmitter
Rayleigh Channel Implementation:
function [rx, h] = rayleigh_channel(tx, N0) tx = tx(:); % ensure column vector h = (randn(length(tx),1) + 1j*randn(length(tx),1))/sqrt(2); % Rayleigh n = sqrt(N0/2)*(randn(length(tx),1) + 1j*randn(length(tx),1)); % AWGN rx = h .* tx + n; end
Receiver Processing:
function z = equalize(rx,h) % Channel equalization z = rx ./ h; end

## Slide 16: Code - Transmitter
Demapping:
function bits_dec = decode_bits(bits_rx, repetition_factor) % Majority vote decoding bits_matrix = reshape(bits_rx, repetition_factor, []); bits_dec = sum(bits_matrix,1) >= ceil(repetition_factor/2); bits_dec = bits_dec.'; % column vector end
Decoding:
function bits = demap_symbols(symbols, modulation) % Demap symbols back to bits switch upper(modulation) case 'BPSK' bits = real(symbols) >= 0; case 'QPSK' bits = zeros(2*length(symbols),1); bits(1:2:end-1) = real(symbols)>=0; bits(2:2:end) = imag(symbols)>=0;

## Slide 17: Code - Transmitter
case '16QAM' symbols = symbols(:); % ensure column vector % Define constellation I_levels = [-3 -1 3 1]; Q_levels = [-3 -1 3 1]; const = zeros(16,1); for k=0:15 bin_k = de2bi(k,4,'left-msb'); bin_nat = zeros(size(bin_k)); bin_nat(1) = bin_k(1); bin_nat(2) = xor(bin_nat(1), bin_k(2)); bin_nat(3) = xor(bin_nat(2), bin_k(3)); bin_nat(4) = xor(bin_nat(3), bin_k(4)); i_idx = bi2de(bin_nat(1:2),'left-msb')+1; q_idx = bi2de(bin_nat(3:4),'left-msb')+1; const(k+1) = I_levels(i_idx)+1j*Q_levels(q_idx); end const = const/sqrt(mean(abs(const).^2)); % Nearest neighbor detection [~, idx] = min(abs(symbols - const.'),[],2); % now safe gray = de2bi(idx-1,4,'left-msb');
Decoding:

## Slide 18: Code - Transmitter
% Reverse Gray bits_mat = zeros(size(gray)); bits_mat(:,1) = gray(:,1); bits_mat(:,2) = xor(bits_mat(:,1),gray(:,2)); bits_mat(:,3) = xor(bits_mat(:,2),gray(:,3)); bits_mat(:,4) = xor(bits_mat(:,3),gray(:,4)); bits = reshape(bits_mat.',[],1); otherwise error('Unsupported modulation type'); end end
Decoding:
BER Compution:
function BER = compute_ber(tx,rx) % Compute Bit Error Rate BER = sum(tx~=rx)/length(tx); end

## Slide 19: Code - Transmitter
for idx = 1:length(SNR_db) %% ----- Noise power ----- EbNo_linear = 10^(SNR_db(idx)/10); N0 = Eb / (EbNo_linear * bits_per_symbol); %% ----- BER without repetition (Normal) ----- tx_symbols_normal = map_bits(Tx_bits, modulation_type); [rx_symbols_normal, h_normal] = rayleigh_channel(tx_symbols_normal, N0); z_normal = equalize(rx_symbols_normal, h_normal); rx_bits_normal = demap_symbols(z_normal, modulation_type); BER_Normal(idx) = compute_ber(Tx_bits, rx_bits_normal); %% ----- BER with repetition (factor 5) ----- Tx_bits_rep = encode_bits(Tx_bits, repetition_factor); tx_symbols_rep = map_bits(Tx_bits_rep, modulation_type); [rx_symbols_rep, h_rep] = rayleigh_channel(tx_symbols_rep, N0); z_rep = equalize(rx_symbols_rep, h_rep); rx_bits_rep = demap_symbols(z_rep, modulation_type); Rx_bits = decode_bits(rx_bits_rep, repetition_factor); BER_Rep5(idx) = compute_ber(Tx_bits, Rx_bits); end
BER Simulation over SNR:

## Slide 20: Code - Transmitter
% PART 3: Plot Results figure; semilogy(SNR_db, BER_Normal, 'b-o','LineWidth',1.5); hold on; semilogy(SNR_db, BER_Rep5, 'r-s','LineWidth',1.5); grid on; xlabel('Eb/No (dB)'); ylabel('Bit Error Rate (BER)'); legend('Normal','Repetition 5'); title(sprintf('%s Performance over Rayleigh Channel', modulation_type));
Result Visualization:

## Slide 21: OFDM System Simulation

## Slide 22: Flat Fading Channel
QPSK achieves lower BER than 16-QAM due to its larger constellation distance
Effect of Coding (Repetition 1/5):
  Fading affects all subcarriers simultaneously.
  All 5 copies suffer the exact same fade. This results in the inability to exploit the multi carrier advantages
  The improvement seen in is purely due to energy of the repetition code

## Slide 23: Flat Fading Channel
Same energy per information bit
Same energy per transmission bit

## Slide 24: Frequency Selective Fading Channel
QPSK achieves lower BER than 16-QAM due to its larger constellation distance
Effect of Coding (Repetition 1/5):
  Fading on different subcarriers is independent
  System is exploiting the multi carrier advantages.
  Repetition code spreads the 5 copies of a bit across different subcarriers.
  The probability of 3 of 5 subcarriers being in a deep fade simultaneously is low.
  Some improvement is due to energy of the repetition code

## Slide 25: Frequency Selective Fading Channel
Same energy per information bit
Same energy per transmission bit

## Slide 26: Code
% ===================== System Parameters ===================== cp = 16; % Cyclic prefix length rate = 1/5; % Coding rate N_fft = 256; % FFT size Eb_N0_dB = 0:2:20; % Eb/N0 range in dB N_OFDM = 10000; % Number of OFDM symbols modulation ='QPSK'; % Modulation type: (BPSK, QPSK, 16QAM) energy_type = 'Same_Per_Trans'; % Energy normalization type channel_type = 'FreqSel'; % Channel type: Flat or Frequency Selective
Parameters:

## Slide 27: Code - Transmitter
function R = generate_data(m, N_fft, N_code) % N_code = 1 mean No coding it applied R = randi([0 1], 1, floor(N_fft/N_code)*m); End
Bitstream Generation:
function R = Encoder(data, m, N_fft, N_code) % N_code = 1 mean No coding it applied encoded_data = repelem(data, N_code); % Padding R = [encoded_data, zeros(1, (m*N_fft)-length(encoded_data))]; End
Encoder:

## Slide 28: Code - Transmitter
function R = Interleaver(mod, data) if isequal(mod, 'BPSK') reshape_tx_data = reshape(data, 8, 32)'; elseif isequal(mod, 'QPSK') reshape_tx_data = reshape(data, 16, 32)'; elseif isequal(mod, '16QAM') reshape_tx_data = reshape(data, 32, 32)'; end R = reshape_tx_data(:)'; end
Interleaver:

## Slide 29: Code - Transmitter
% Mapper mapper_output = Mapper(interleaver_output, modulation); % ifft ifft_output = ifft(mapper_output, N_fft); % cyclic extension cyclic_output = [ifft_output(end-cp+1:end), ifft_output];
Mapper, ifft and cyclic extension:

## Slide 30: Code - Channel
Channel
function [Channel_Output, H] = Channel(data, m, Eb_N0_dB, N_code, N_fft, cp, channeltype, energy_type) % Noise segma = sqrt((1/2)./10^(Eb_N0_dB/10)); Eb_actual = (sum(abs(data).^2)/length(data))/m; noise = sqrt(Eb_actual) * segma * (randn(size(data)) + 1j*randn(size(data))); if isequal(energy_type, 'Same_Per_Info') noise = sqrt(N_code) * noise; end if isequal(channeltype, 'Flat') % Flat fading channel H = sqrt(1/2)*(randn(1) + 1j*randn(1)); Channel_Output = H*data + noise; else

## Slide 31: Code - Channel
% Frequency selective channel H = sqrt(1/2)*(randn(1, N_fft) + 1j*randn(1, N_fft)); % Remove cyclic extension data_cp_removed = data(cp+1:end); % Frequency domain data_freq = fft(data_cp_removed, N_fft); % Applay Freqency Selctive Channel ch_out_freq = data_freq .* H; % Time domain ch_out = ifft(ch_out_freq, N_fft); % Add cyclic extension ch_out = [ch_out(end-cp+1:end), ch_out]; %Add Noise Channel_Output = ch_out + noise; end end

## Slide 32: Code - Receiver
% Remove cyclic extension remove_cyclic_output = channel_output(cp+1:end); % fft fft_output = fft(remove_cyclic_output, N_fft); % channel equalization channel_equ = fft_output ./ H;
Remove cyclic extension, fft, channel equlization:

## Slide 33: Code - Receiver
% De-Mapper demapper_output = Demapper(channel_equ, modulation); % De-Interleaver deinterleaver_output = DeInterleaver(modulation, demapper_output); % Decoder decoder_output = Decoder(deinterleaver_output, m, N_fft, N_code);
De-Mapper, De-Interleaver and Decoder:

## Slide 34: Thank you
Team 46